## Slide 1: FT8: Digital DXing on Dead Bands
SEMDXA Monthly Meeting
November 9, 2017
Larry Gauthier, K8UT

## Slide 2: FT8: DXing on Dead Bands
Unless you live under a rock, you’ve heard about FT8
Notes: Comment about popularity of FT8
ClubLog report that more FT8 uploads in September ‘17 than for SSB and CW combined

## Slide 3: FT8: DXing on Dead Bands
Some Say: The Greatest Thing Since…

## Slide 4: FT8: DXing on Dead Bands
Others Say: The End of Ham Radio as We Know It

## Slide 5: FT8: DXing on Dead Bands
What is it?
  For the Engineer:
    A communications protocol based on
      Multi-Tone Frequency Shift Keying (MFSK)
      Using 8 tones
      Spaced at 6.25 Hz
      Occupying 50 Hz of bandwidth
      Transmitting for (79*1920/12000) = 12.64 seconds
              Formula at https://sourceforge.net/p/wsjt/wsjt/8021/
      With a 75 bit message + 12 bit CRC, and LDPC FEC*
      *Cyclic Redundancy Check and Low Density Parity Check Forward Error Correction
  Reference: QST, November 2017, page 34 Work the World with WSJT-X, Part 2: Codes, Modes, and Cooperative Software Development

## Slide 6: FT8: DXing on Dead Bands
What is it?
  For the Rest of Us:
    A multi-platform (Windows, Linux and Mac)
    Non-conversational (rag-chewers need not apply)
    Auto-sequencing (step away from the keyboard)
    Digital mode (a’ la JT65, PSK31, Olivia, Hell… et al)
    With (relatively) short transmissions of 15 seconds
    Designed for low signal conditions (dead HF bands)
    In short – WSJT / FT8 is just very cool and a lot of fun

## Slide 7: FT8: DXing on Dead Bands
Who Did This?
  Initially written by
    Steve Franke K9AN
    Joe Taylor K1JT
    …now maintained by a world-wide team of developers
  FT8 stand for “Franke-Taylor 8” MFSK modulation
When Did This Happen?
  WSJT-X with FT8 was first released on June 29, 2017
    Multiple iterations of beta Release Candidates (RC)
    Finally released to General Availability on October 27, 2017
Notes: Note significance of the explosive adoption of the protocol despite still being a beta program

## Slide 8: FT8: DXing on Dead Bands
Where Can I Get It?
  FT8 (the protocol) is included in WSJT-X (the program)
  WSJT-X v1.8.0 is available from
    https://physics.princeton.edu/pulsar/k1jt/wsjtx.html
Will I Need Help?
  It depends. Probably…
    Read the documentation available on the website
    Join the Yahoo User Group: wsjtgroup
    Watch Youtube videos
    Don’t be afraid to get on the air and experiment
      You will make mistakes. I certainly have!

## Slide 9: FT8: DXing on Dead Bands
What Else Will I Need?
  Working transceiver and antennas
  PC with Soundcard (s)
  Multiple monitors (?)
  Audio / CAT / PTT interface between PC and rig
  Some method for time synchronization
Recommended: JTAlert-X companion software
  Audio and visual alerts, assists DXCC award hunting
  Can forward QSOs to your general logging program
    HRD, Logger32, DXLab, N1MM+… others
  Includes an internet Chat feature
      Which comes as a bit of a surprise the first time the Chat window pops up
Notes: Note benefit of two soundcards – one for Windows noises, other for digital modes
Otherwise need to disable Windows noises if you only have one soundcard
Need for lots of monitor real estate, especially if running WSJT in parallel with your general logging program
JTAlert’s “CQ,” “New State,” “DX” audio alerts – permits multi-tasking in the Ham Shack
Briefly describe operation of JTAlert chat feature

## Slide 10: FT8: DXing on Dead Bands
If the Bands are Dead, Where Should I Listen?
Prescribed frequencies from 160 -to- 6
      1.840, 3.573, 7.074, 10.136, 14.074,
      18.100, 21.074, 24.915, 28.074, 50.313
Do I need to memorize this stuff?
  No! Just press the band button to QSY to the right QRG

## Slide 11: FT8: DXing on Dead Bands
If the Bands are Dead, Where Should I Listen?
Prescribed frequencies from 160 -to- 6
      1.840, 3.573, 7.074, 10.136, 14.074,
      18.100, 21.074, 24.915, 28.074, 50.313
Do I need to memorize this stuff?
  No! Just press the <Frequency> button for each band
Soooo… what does this thing look like?

## Slide 12: FT8: DXing on Dead Bands
Notes: Acknowledge that initial glimpse of WSJT-X is overwhelming

## Slide 13: FT8: DXing on Dead Bands
Notes: !!Even Scary!! – but proceed to describe the two major sections of the application in the next two slides

## Slide 14: FT8: DXing on Dead Bands
WSJT-X The Graphic Display
CIRCLE = Transmit (red) and Receive (green) positions
Notes: Explain the significance of all circled items
Talk about bandwidth from the radio – USB or digital mode, filters, notches
Received display in 15 seconds intervals
Display Settings are mostly set-and-forget, unless using AGC = OFF {which is the recommended setting} in which case you may need to constantly adjust the display Zero and Gain settings from band-to-band
Tx & Rx indicators – Simplex vs Split

## Slide 15
WSJT-X Control Display
Notes: Explain major elements of the controls
ESP:
Drop-down band selector
Rx Signal strength db indicator {should be around 30db}
Pwr slider bar = does NOT really adjust power but audio modulation. On an Elecraft K3 this is the wrong way to control power because of its unique ALC circuits
Enable Tx has adjustable auto-shutoff ( after calling CQ x times it will auto-stop)
Hold Tx Freq (split operation)
Auto Seq ecplained in next two slides
Call 1st gives priority to Rx frequency
Tx Even/First (0 & 30) is the convention for calling CQ

## Slide 16
WSJT-X Auto-Sequence Controls
Notes: Double-clicking on a callsign or pressing <Enable Tx> will populate the Generated Messages
Override the next auto-sequence transmission by clicking on the Tx# buttons
5th message can be replaced with free-text entry - up to 13 characters
Message sequence skips based on Run station (CQ caller) and S&P station (respondent)

## Slide 17
Auto-Sequence Options
  Force a different message
    Click in the <Now> column
  Use new “shortcut” RR73
  Send a pre-defined message
    From a list you create
  Send a free-text message
    From the keyboard
    Max 13 characters How fast can you type? You’ve got 15 seconds!
WSJT-X Auto-Sequence Details
Notes: New convention to shorten sequence by one exchange with RR73 vs RRR when signals are reliable. Gaining popularity
Comment about freetext and difficulty in getting them prepared within 15 second listen interval

## Slide 18: WSJT-X: Two Video Examples
Stand-Alone Operation
  Easier configuration
  Stores contacts to its own log
  Can export to ADIF after-the-fact
Log Integration, using JTAlert-X utility app
  More difficult configuration
  Communicates using UDP packets
  Stores to both WSJT-X and your logging file
  Reportedly works with:
    Logger32, HRD, DXLab, N1MM+, Log4OM, others…
Notes: Comment about shortcomings of the WSJT log for Award Tracking - postal bureau and direct QSLing, ClubLog, eQSL and LoTW integration

## Slide 19
WSJT-X Stand-Alone Video
Show video now…
Notes: Stop the video at each stage of the auto-sequence to explain what is happening and how to tell if things are working or broken.
TX/RX indicator moves, <Enable Tx> button lights, Receive/Transmit goes from green to yellow, Progress bar (seconds to go indicator) advances, auto-sequence radio button increments

## Slide 20
WSJT-X Log Integration Video
Show video now…
Notes: Describe the DXLab screens and how they will interact with WSJT in each phase of the sequence.
Mention that this is relatively robust integration as compared to the simple “after the QSO, add a record” integration available in N1MM+.
Stop the video at each stage of the auto-sequence to explain what is happening and how to tell if things are working or broken.
TX/RX indicator moves, <Enable Tx> button lights, Receive/Transmit goes from green to yellow, Progress bar (seconds to go indicator) advances, auto-sequence radio button increments
Talk about variability in signal reports. “One Way Skip” – especially at band openings. Adjust power levels accordingly.

## Slide 21: FT8: The Devil in the Details
Time synchronization is critical. PC clocks are inaccurate
  Tx is 12.64s out of 15 seconds. Clock should be within 1 second
  You need an NTP, WWV, GPS, Cellular or ??? solution
Never-ending debate over Split versus Simplex operation
  You need to understand how to operate both
  For Run, I work the guy wherever he returns my CQ (usually Simplex)
  For S&P, both. Initially call Simplex, resort to Split in QRM or a pile-up
Understand the 13 character limit for free-text messages
  But Generated messages can be longer than 13 characters (??)
Be prepared for non-conforming callsigns: 3XY4D, VX7150
  They “break” auto-sequencing, require manual operation and free-text
Contest and DXpedition operation
  Uncharted waters on HF… stay tuned
Notes: Split vs Simplex = do the math for the audience: 2.5KHz wide bandwidth divided by 50 Hz signal + 10 Hz spacing = about 40 simplex signals. Half that number if all are split?
What happens when a DXpedition attracts 1000 simultaneous callers?
Callsign recognition is a well defined algorithm, but cannot tolerate exceptions. ( unlike most logging programs, which use popular lookup CTY file from AD1C)
Double-clicking and auto-sequencing DO NOT work unless WSJT recognizes a callsign
13 Character free-text limits? Advise users that they will notice Generated messages longer than 13 characters – how does that work? WSJT tokenizes and complresses standard expressions like CQ, 73, EU, NA, DX, grid squares

## Slide 22: FT8: Summary
Question:
Are the bands really dead?
Answer: Not if you’re running FT8!

## Slide 23: FT8: 12 Meters, Saturday 8am
Notes: Visually empty 12 meter band, early morning before this band normally opens

## Slide 24: FT8: 12 Meters, Saturday 8am
Notes: Despite that, at least 6 signals in the waterfall. 8 DXCC callsigns in the Band Activity panel

## Slide 25: FT8: 17 Meters, Monday 8am
Notes: Another dead band except for FT8 segment. 8am on a Monday morning

## Slide 26: FT8: 17 Meters, Monday 8am
Notes: At least 25 signals in the waterfall display. 14 DXCC callsigns in the Band Activity panel

## Slide 27: FT8: 20 Meters, Saturday 8am
Notes: 20 meters during a CW contest weekend. Band is crowded with signals

## Slide 28: FT8: 20 Meters, Saturday 8am
Notes: At least 25 signals in the waterfall. 10 DXCC callsigns in the Band Activity panel

## Slide 29: FT8: 160 Meters, Monday 6am
Notes: 160 meterrs. Typicall Monday morning activities. A handfull of signals on the air.

## Slide 30: FT8: 160 Meters, Monday 6am
Notes: 11 signals in the waterfall. No DX at this late hour, but many WAS states represented.

## Slide 31
K8UT’s 3 Month Results
Total = 780 FT8 QSOs
Notes: K8UT’s brag slide: WAS and DXCC confirmed on LoTW in 90 days

## Slide 32: FT8: Digital DXing on Dead Bands
Larry Gauthier, K8UT
Thank You!